## Slide 1: The 18th summer course of Behavior Modeling Final presentation
University of Tokyo team A
Takuya Iizuka (M1)
Kenta Ishii (M1)
Shoma Dehara (M1)
Miho Yonezawa (M1)
マルコフ決定過程に基づく経路選択行動のパラメータ推定
—自動車・自転車交通施策の検討—
Evaluation of car/bicycle traffic measures with a link choice model

## Slide 2: 1. Background
Area: 松山市 Matsuyama city
Population: 512479 (2018.1.1.)
Area: 429.06 m2
Many people use private car.
City projects are underway to increase activity in the central city.
http://udcm.jp/project/

## Slide 3: 2. Basic Analysis
Chart: Representative Mode Choice in Matsuyama (n=7107)
| Car | Motorcycle | Train | Bus | Taxi | Bicycle | Walk | Other
 | 3758 | 798 | 152 | 41 | 34 | 1247 | 1061 | 50
※経路情報が得られたトリップを抽出
Mode Choice
Data: Matsuyama PP (2007 Feb.19 – Mar.23)
High rate of Car & Bicycle use
Car & Bicycle paths are overlapping.
→By providing bicycle lanes, traffic accidents can be suppressed !!

## Slide 4: 2. Basic Analysis
Traffic Volume in the center of Matsuyama
Car Trip
Bicycle Trip
Center Station
City Hall
Dogo Onsen
JR Station
Center Station
City Hall
Dogo Onsen
JR Station
Most part of the center of Matsuyama, the car & bicycle trips are separated.
At some roads, car & bicycle trips are overlapping!!

## Slide 5: 2. Basic Analysis
Car & Bicycle traffic of each link
The smaller the traffic of the car, the more traffic of the bicycle.
On links with heavy car traffic, sidewalks are maintained, increasing bicycle traffic.

## Slide 6: 3. Target
Our Goal
To clarify what is important element in the route choice behavior of car & bicycle
To simulate transport policy and to verify the sensitivity of each parameter
For Simulation
Characteristics of each link (length, width, etc.) affect travelers’ behavior.
→ We adopt Link Base Route Choice Model for analysis.

## Slide 7: 4. Model
Different Estimation method
Behavior model;
RL model
Inverse Reinforcement Learning (IRL)
compare
parameter
Estimation
Link based route choice model
link length
lanes
right turn dummy

## Slide 8: 4. Model
Sequential Route Choice Model: Recursive Logit model (RL) (Fosgerau et al., 2013)
Graph:
: set of links
: set of nodes
absorbing state
Utility Maximization problem
An instantaneous utility
At each current state , a traveler chooses an action (next link).
: error term (i.i.d. Gumbel distribution)
: scale parameter
: discount rate
An expected downstream utility :value function
from the selected state to the destination link
The value function is defined by the Bellman equation (Bellman, 1957);
Link choice probability

## Slide 9: 4. Compared IRL with RL
: discount rate ()
: expected reward
( )
Bellman equation
Transition state

## Slide 10: 4. Compared IRL with RL
The estimation method : Recursive Logit model (RL) -NPL
Parameter
Value function
Choice
probability
Likelihood
Convergence test
estimated
Parameter
Yes
No
Reward (Instantaneous utility):
The algorithm for calculating fixed point of value function
Convergence test

## Slide 11: 4. Compared IRL with RL
The estimation method : Max entropy - Inversed Reinforced Learning (IRL)
Parameter
Reward
Policy
( value)
Likelihood
estimated
Parameter
No
Reinforced Learning
Reward:
Problem
where is the path of expert
is the feature relating to link
st.
Convergence test
Yes

## Slide 12: 5. Estimation Result
IRL estimation (car)
Variables | Parameters | t-Value
Link Length | -0.07 | -9.72**
Right-Turn | -1.02 | -8.53**
Lanes | -0.37 | -5.64**
L(0) | -2080.67
LL | -1117.10
Rho-Square | 0.46
Adjusted Rho-Square | 0.46
(given)
RL estimation (car)
Variables | Parameters | t-Value
Link Length | -0.03 | -1.33
Right-Turn | -0.80 | -6.49**
Lanes | 0.37 | 2.76**
L(0) | -1179.29
LL | -1147.00
Rho-Square | 0.03
Adjusted Rho-Square | 0.02
0.47 (given)

## Slide 13: 5. Estimation Result
Recursive Logit estimation (bicycle)
Variables | Parameters | t-Value
Link Length | -0.00 | -6.21**
Right-Turn | -0.19 | -3.67**
Car Traffic | -14.37 | -0.14
β | 0.00 | 15.15**
L(0) | -4093.90
LL | -3861.56
Rho-Square | 0.06
Adjusted Rho-Square | 0.06

## Slide 14: 5. Simulation and Evaluation
Car traffic
Car Assignment
Bicycle Assignment
Network Policy

## Slide 15: 5. simulation
 | Without policy | With policy (rode lanes are reduced)
Private car user | -2639 | -2638
Bicycle user | -9297 | -1147
Private car/bicycle user’s logsum value with/without policy
Reduce the lanes of large bicycle traffic links
←Bicycle traffic
Policy
Increased!!

## Slide 16: 6. Future works
Policies decided by Two-stage optimization
To decide the policy
by calculating the fixed point of demand of cars and bicycles
Policy
change
Demand
change
Variables is changed
Consumer surplus

## Slide 17: 5. Estimation Result
IRL estimation (car)
Variables | Parameters | t-Value
Link Length | -0.00572672 | -32.43800**
Right-Turn | -1.3377633 | -31.31264**
Lanes | -0.2701062 | -15.55912**
L(0) | -20896.98
LL | -11539.03
Rho-Square | 0.4478132
Adjusted Rho-Square | 0.4476696

## Slide 18: 5. To do
For the final presentation
Make RL code running with car & bicycle trips (with reduced network)
Compare other estimation method such as IRL: Inverse Reinforcement Learning
Consider various patterns of traffic policy.

## Slide 19: 4. Frame & Model
Upper Problem: traffic network
reduction of vehicle lanes (pedestrian/bicycle only)
traffic volume of each link
Lower Problem: route choice behavior
Car
Bicycle
Assign each OD volume
network
Parameter Estimation
Behavior model;
RL model
parameter
Estimation
Policy Simulation
link length
lanes
right turn dummy

## Slide 20: 4. Frame & Model
Upper Problem: traffic network
reduction of vehicle lanes (pedestrian/bicycle only)
traffic volume of each link
Lower Problem: route choice behavior
Car
Bicycle
Assign each OD volume
network
Different Estimation method
Behavior model;
RL model
Inverse Reinforcement Learning (IRL)
compare
parameter
Estimation
Policy Simulation
Link based route choice model
link length
lanes
right turn dummy

## Slide 21: 5. Simulation and Evaluation
Feasibility of set the bicycle lanes
Policy: Providing bicycle lanes at some links